## Slide 1
SSP Manual
Pages
9 to 19
MODULE 1:
PREPARE FOR SANITATION SAFETY PLANNING

## Slide 2
1.1 Define the SSP area and lead organization
1.2 Assemble the SSP team
1.3 Establish SSP priorities
Agreed SSP area, leadership and priorities
A multidisciplinary team representing the sanitation chain for development and implementation of SSP.
PREPARE FOR SANITATION SAFETY PLANNING

## Slide 3
This step helps to drive and sustain the SSP process, and ensures that the scope is manageable and understood by all stakeholders.
… within an administrative area
… within the service area of a sanitation utility or a service provider
SSP could be carried out…
Define the SSP area and lead organization
STEP 1.1
SSP Manual
Pages
10 to 12

## Slide 4
Define the SSP area and lead organization
STEP 1.1
The SSP area is determined by the area administered by the local authority.
All the existing sanitation systems and all sanitation steps within the sanitation service chain should be included.
The lead organization should be the local authority with the mandate for oversight of sanitation service provision.
A team leader should be appointed to drive the SSP process
When SSP is initiated by a municipality, district or administrative unit
SSP Manual
Example 1.1
Page 11

## Slide 5
Define the SSP area and lead organization
STEP 1.1
EXAMPLE: When SSP is initiated by a municipality, district or administrative unit (1/3)
-System 1: Flush toilets with sewerage and offsite wastewater treatment (area in blue)
-System 2: Flush toilets with septic tanks and effluent infiltration and offsite fecal sludge disposal (area in yellow)
-System 3: Dry or flush toilets with onsite disposal or offsite disposal (area in green)

## Slide 6
Define the SSP area and lead organization
STEP 1.1
When SSP is implemented by sanitation service providers
SSP is implemented to ensure that:
-the sanitation systems under their responsibility are safely operated.
-their products (e.g. treated water, dried sludge, fertilizers, etc.) do not pose health risks during disposal or use.
SSP Manual
Examples 1.2
to 1.4

## Slide 7
Define the SSP area and lead organization
STEP 1.1
Container-based sanitation (CBS) system in a densely populated area in Cap Haitian in Haiti: area and lead organization
EXAMPLE: When SSP is implemented by sanitation service providers
SSP Manual
Example 1.3
Page 11
Photos: Emmanuel Antoine, SOIL
TEAM LEADER: A program officer

## Slide 8
Define the SSP area and lead organization
STEP 1.1
Two or more administrative areas are involved:
Sanitation activities are in different administrative areas. For example:
-A wastewater treatment plant (WTP) is in an urban area.
-The WTP effluent is reused in agricultural lands located in a different administrative area and overseen by a different authority.
SSP Manual
Example 1.5
Page 12
TEAM LEADER: A coordination team

## Slide 9
To ensure broad stakeholder commitment to design and implement the entire SSP process.
In sanitation systems this is particularly important, as responsibility along the sanitation chain is seldom the responsibility of one organization.
SSP requires clear and active leadership to succeed.
Assemble the SSP team
STEP 1.2
SSP Manual
Pages
12 to 17

## Slide 10
Assemble the SSP team
STEP 1.2
Appoint a SSP team leader
A team leader should be identified and appointed at the outset who will play a critical role in:
-communicating about SSP;
-mobilizing stakeholders; and
-leading development, implementation and updates of the SSP.
The team leader should have:
Authority
Organizational and interpersonal skills
Time
If the skills are not available locally: explore opportunities for external support
Sufficient knowledge

## Slide 11
Assemble the SSP team
STEP 1.2
Form the SSP team
The team should include:
managers within the relevant organizations
Key representatives of organizations in charge of sanitation steps outside the responsibilities of the lead institution;
people with public health expertise;
representatives of key exposure groups;
External experts and independent members (universities, etc.)
The team should be able to:
Recognize all the hazards and hazardous events
Rate the risk
Drive improvements in all areas of sanitation
SSP Manual
Example 1.7
Page 14

## Slide 12
Mix of skills in technical, health and climate topics
WHO Guidelines on Sanitation and Health, Recommendation 4:
The health sector should fulfil core functions to ensure safe sanitation to protect public health. Mandate of local health authorities includes:
Health protecting norms and standards
Health surveillance and response
Sanitation in health programme delivery
Sanitation behaviour change
Health Authorities (e.g. Environmental Health and Public Health Authorities)
Climate change specialists
Climatology
Hydrology
Disaster or emergency management
Assemble the SSP team
STEP 1.2
WHO Guidelines
Chapter 2
Pages 18-20

## Slide 13
Assemble the SSP team
STEP 1.2
Define and record roles of the individuals on the team
Responsibilities should be divided among the team members at the start of the process, and roles clearly defined and recorded.
SSP Manual
Tool 1.1
Page 15

## Slide 14
Assemble the SSP team
STEP 1.2
Stakeholder analysis for large or complex SSPs
Process of identifying and characterizing stakeholders, and planning for their participation.
SSP Manual
Tool 1.2
Page 16
Stakeholders are individuals or organizations that: have direct control, have some influence, are affected by and are interested in sanitation systems.

## Slide 15
Assemble the SSP team
STEP 1.2
SSP Steering Committee for large or complex SSPs
Representative body with combined oversight of each step of the sanitation service chain, from toilet, including on-site containment, to conveyance through sewers or vacuum trucks, to treatment and disposal or reuse.
SSP Manual
Example 1.9
Page 17
Senior representatives from relevant authorities
Senior representatives of the implementation partners
WHO Guidelines on Sanitation and Health :
Establish local government coordination groups with senior representation from all relevant local government departments and implementation partners to align and coordinate sanitation activities.
WHO Guidelines
Chapter 2
Pages 21-22

## Slide 16
Assemble the SSP team
STEP 1.2
SSP Steering Committee for large or complex SSPs
Leadership and oversight of the entire process.
Agreed priority areas for SSP.
Engagement with, and get commitment of, senior management of the lead organization.
Secured financial and resource commitment.
Policy dialogue and amendment as needed to create an enabling environment for safe sanitation service delivery.
Steering committees provide:

## Slide 17
Assemble the SSP team
STEP 1.2
Management and financial considerations
sampling and testing
data collection
field investigations
The SSP effort will require an in-kind commitment of time and some direct costs during the preparation phase for:
Management support will be needed for the SSP process to allocate staff time and any start-up funding needed

## Slide 18
This step establishes the priority sanitation challenges for SSP and makes the SSP process manageable.
Risk-based tools can be used to analyse the situation, to identify and reach agreement on SSP priorities:
Excreta flow diagrams (SFDs)
Establish SSP priorities
STEP 1.3
SSP Manual
Pages
17 to 19
The SaniPath Exposure Assessment Tool

## Slide 19
Establish SSP priorities
STEP 1.3
Excreta flow diagrams (SFD)
These help to establish priorities by graphically showing proportions of excreta in a city or town that are not safely managed at each step of the sanitation chain:
Red or green arrows signal where the greatest risks lie and help city stakeholders identify the highest risks for management using SSP
SSP Manual
Guidance Note
1.2. Page 18
Source: Blackett, Hawkins & Heymans (2014) (example of an SFD in Dakar, Senegal).

## Slide 20
Establish SSP priorities
STEP 1.3
The SaniPath Exposure Assessment Tool
This helps to establish priorities by identifying the primary pathways (e.g. open drain, produce, drinking-water) of exposure and the magnitude of contamination in a locality.
People plots allows easy visual comparison of exposure across different pathways, neighbourhoods or populations. Each red figure represents 1% of the population that is exposed to faecal contamination.
SSP Manual
Guidance Note
1.3. Page 19
Source: For more information, visit the Sanipath Portal (https://www.sanipath.org) hosted by the Center for Global Safe WASH at Emory University

## Slide 21
Establish SSP priorities
STEP 1.3
WHO Guidelines recommendations
WHO Guidelines
Chapter 2
Pages 11-16
Prioritize:
Areas with high frequency of open defecation.
Communities where toilets are poorly constructed, unsafe and do not safely contain excreta.
Entire communities: everyone should be using a toilet to achieve health gains.
Include:
Shared and public toilets, in case household level access is not possible.
Schools, health care facilities, workplaces and public places.
1. Universal safe toilets that contain excreta
2. Safe sanitation chain
Include:
Full sanitation chain from waste generation to reuse or disposal: toilet, containment, transport, treatment, end use/disposal.
All waste streams at all points of the sanitation system, in particular the waste streams that receive inadequate or unknown treatment (for instance, faecal sludge).
Consider:
Sanitation workers, who are at high risk from faecal pathogens exposure.

## Slide 22
Establish SSP priorities
STEP 1.3
Other considerations:
Districts and neighbourhoods with high reported or suspected sanitation- related diseases.
Communities where toilets are poorly constructed, unsafe and do not safely contain excreta or drainage systems are inadequate.
Nonregulated sanitation service chains (e.g. faecal sludge management), and waste streams that receive inadequate or unknown treatment.
Sanitation systems that historically, or can be envisaged to, have a high susceptibility to climate-related events (e.g. sewer overflows near recreation areas or water supplies, overflowing of pit latrines).
Water supply catchments and intakes affected by wastewater, excreta or greywater.
Areas with high formal or informal wastewater use activities (e.g. agriculture, aquaculture).

## Slide 24
Step 1.1. Define the SSP area and lead organization
The SSP area is determined by the territorial division covered by the Newtown municipality.
The two existing sanitation systems and all sanitation steps within the sanitation service chain are considered.
Module 1: Prepare for SSP
SSP area
Newtown Sanitation Department (NSD)
Lead organization
Step 1.2. Assemble the SSP team
Head of Planning of the NSD
SSP team leader
Senior engineer who oversees system 1, a senior engineer who monitors system 2, and an Environmental Health Officer who coordinates environmental health programmes in Newtown.
SSP core team

## Slide 25
Step 1.1. Define the SSP area and lead organization
The SSP team decided to prioritize system 2 (flush toilets with septic tanks and effluent infiltration, and off-site faecal sludge disposal).

## Slide 26
Use participant’s worksheet:
Module 1
Within your groups:
Define the area in which you will develop the SSP during this training.
Describe the SSP area.
Decide who should be the leader
Which persons should be in the SSP team?
Work as a group, but record on your individual worksheets.
Applying Module 1

## Slide 27
MODULE 1:
PREPARE FOR SANITATION SAFETY PLANNING