## Slide 1
SSP Manual
Pages
21 to 32
-PART 1-
MODULE 2:
DESCRIBE THE SANITATION SYSTEM

## Slide 2
2.1 Map the system
2.2 Characterize the system flows
2.3 Identify exposure groups
2.4 Gather supporting information
2.5 Confirm the system description
A map and description of the sanitation system.
An understanding of the constituents (excreta and mixed waste) in flows at all steps of the sanitation system.
Identification and characterization of exposure groups.
An understanding of the factors affecting the performance and vulnerability of the system
A compilation of all other relevant information.
DESCRIBE THE SANITATION SYSTEM

## Slide 3
To understand the source and path of flows through the system. This is critical in the later assessment of exposure groups at risk.
Map the system
STEP 2.1
WHO Recommendations
Recommendation 2: Ensure universal access to safe systems along the entire sanitation service chain.
Consider full sanitation chain from waste generation to reuse or disposal: toilet, containment, transport, treatment and end use/disposal.
WHO Guidelines
Chapter 2
Pages 11-16

## Slide 4
Safe sanitation systems
Sanitation systems are a combination of technologies and services that, when linked and properly managed, can form a safe chain.
Map the system
STEP 2.1
WHO Recommendations – Chapter 3
WHO Guidelines
Chapter 3
Pages 29-58

## Slide 5
Dry Toilet
Urine Diverting Dry Toilet
Pour-Flush Toilet
Flush Toilet
Toilet
User interface with the sanitation system, where excreta is captured, and can incorporate any type of toilet seat or latrine slab, pedestal, pan or urinal.
Map the system
STEP 2.1
WHO Guidelines
Chapter 3
Page 31

## Slide 6
Single VIP
Dehydration Vaults
Septic Tank
Composting Chamber
Urine storage tanks
Only relevant to non-sewered sanitation systems and refers to the container, usually located below ground level, to which the toilet is connected.
Containment-storage/
treatment
Map the system
STEP 2.1
WHO Guidelines
Chapter 3
Page 34

## Slide 7
Conventional Gravity Sewer
Small-Bore Sewer
Simplified Sewers
Human-Powered Emptying and Transport
Motorised Emptying and Transport
Movement of wastewater or faecal sludge from a containment technology to off-site treatment, and/or end use/ disposal.
Conveyance/emptying
transport
Map the system
STEP 2.1
WHO Guidelines
Chapter 3
Page 39

## Slide 8
Technologies for containment and storage/treatment of wastewater and faecal sludge on-site.
Technologies for the treatment of wastewater (containing one or more of blackwater, brown water, greywater or effluent) treated off-site.
Technologies for the treatment of sludge off-site.
Process(es) that changes the physical, chemical and biological characteristics or composition of faecal sludge or wastewater so that it is of a quality that is fit for purpose for the intended next use or disposal.
Treatment
Map the system
STEP 2.1
WHO Guidelines
Chapter 3
Page 44

## Slide 9
Application of compost
Irrigation
Aquaculture
Soak pit
Leach field
Land application
Surface disposal
Technologies and methods by which treatment products are ultimately discharged into the environment, either as end use products or reduced-risk materials.
Reuse / disposal
Map the system
STEP 2.1
WHO Guidelines
Chapter 3
Page 49

## Slide 10
Compendium of sanitation systems and technologies
TILLEY, E.; ULRICH, L.; LUETHI, C.; REYMOND, P.; ZURBRUEGG, C. (2014): Compendium of Sanitation Systems and Technologies. 2nd Revised Edition. Duebendorf, Switzerland: Swiss Federal Institute of Aquatic Science and Technology (Eawag).
www.eawag.ch
https://sswm.info/perspective/sanitation-systems-perspective
Sustainable Sanitation and Water Management Toolbox
TIP
For more information about sanitation systems and technologies
Map the system
STEP 2.1

## Slide 11
Simplified drawings or free-flowing sketches
Map the system
STEP 2.1
SSP Manual
Example 2.1
Page 25

## Slide 12
System process diagram
Map the system
STEP 2.1
SSP Manual
Example 2.2
Page 26
EXAMPLE: Map of system consisting of a dry or flush toilet with pit, liquid effluent infiltration and off-site treatment of faecal sludge for reuse

## Slide 13
Map the system
STEP 2.1
SSP Manual
Guidance Note
2.1
Page 24
Identify all the steps of the sanitation service.
Include all sources of system flows.
Ensure that the fate of all used and disposed of parts of the system flows have been accounted for.
Identify areas in which faecal sludge is being dumped legally and illegally.
Identify areas where open defecation is known to occur.
Identify public and shared toilets that serve a considerable proportion of the community.
Include drinking-water sources where this is relevant to the system or could be affected by the sanitation system.
TIP
Checklist of issues to consider when developing a system map

## Slide 14
Establish the path of different of system flows through the sanitation system
Map the system
STEP 2.1

## Slide 15
This step involves collecting key quantitative information, and examining the microbiological, physical and chemical constituents of flows along the sanitation system.
Characterize system flows
STEP 2.2
SSP Manual
Guidance Note
2.2
Page 28
Focus on excreta-related inflows and effluents in each step of the system.
Key information:
  flow rates, where known, including for different seasons, or different levels of rainfall, in the context of potential climate change impacts; and
  capacity or design loading of components, where known (e.g. treatment plant flow or loading limits, transfer system capacities).
Factors to consider when characterizing system flows

## Slide 16
Characterize system flows
STEP 2.2
SSP Manual
Tool 2.1
Page 29
Use the template to characterize system flows:

## Slide 17
A biological, chemical or physical constituent that can cause harm to human health.
Hazards
Biological
Chemical
Physical
Microbiological pathogens:
Bacteria
Viruses
Protozoa
Helminths
Vector-borne
Heavy metals in sludge or biosolids
Herbicides and pesticides
Sharps (e.g. needles)
Odours
Physical injury from equipment
Characterize system flows
STEP 2.2

## Slide 18
Step 2.1. Map the system
Module 2: Describe the sanitation system

## Slide 19
Step 2.1. Map the system

## Slide 20
Step 2.2. Characterize system flows

## Slide 21
Applying Steps 2.1 and 2.2 to your SSP
Use participant’s worksheet 2 for instructions: Module 2
Within your groups:
Map your sanitation system
GROUP WORK
Establish the path of different waste fractions through the sanitation system
Characterize system flows
Make sure you include all by-product waste streams that are part of your SSP system.

## Slide 22
This step identifies and characterizes exposed groups in terms of who they are, how many there are, where are they in the system and how exposure occurs.
Identify exposure groups
STEP 2.3
People who might be exposed to sanitation –related health hazards.
Exposure groups categories:
L= Local community
U= Sanitation systems users
SSP Manual
Guidance Note
2.3
Page 30
WC= Wider community
F= Farmers
W= Sanitation workers
WC= Consumers

## Slide 23
Identify exposure groups
STEP 2.3
SSP Manual
Example 2.4
Page 31

## Slide 24
Identify exposure groups
STEP 2.3
SSP Manual
Tool 2.2
Page 32
Use tool 2.2 to characterize exposure groups

## Slide 25
Step 2.3. Identify exposure groups

## Slide 27
Applying Step 2.3 to your SSP
Use participant’s worksheet 2 for instructions. Within your groups:
Identify exposure groups in your maps
GROUP WORK
Characterize exposure groups.

## Slide 28
Sharing groups results of implementation of Module 1 and Steps 2.1 to 2.3

## Slide 29
SSP Manual
Pages
32 to 37
Let’s continue with module 2!
-PART 2-

## Slide 30
To identify the relevant health hazards to which our exposure groups are exposed.
For that, we collect and document information about the context (the reality) in which the sanitation system exists.
Gather supporting information
Potential hazards:
Relevant hazards:
Actual presence of the pathogens in the community
Actual performance of the treatment system… etc.
STEP 2.4

## Slide 31
Regulatory requirements
Relevant laws and by-laws
Effluent discharge quality standards
Guidelines for climate change preparedness or disaster planning
Demographics and land use patterns
Demographics, land use
Formal and informal settlements
Areas predicted for high population growth
Examples of data to be collated
Gather supporting information
STEP 2.4
SSP Manual
Guidance Note
2.4, Page 33
System management and performance
Monitoring and surveillance records
Epidemiological data
Types and amount of products produced
Changes related to climate and weather
Seasonal changes and impacts on loadings
Seasonal crop and harvest data
Additional inflows during heavy rains
Changes in water usage due to scarcity

## Slide 32
Waste fractions from Step 2.2
Potential health hazards
Contextual and health data
Identify relevant health hazards
Use epidemiological and environmental data where available.
Let’s recap:
For example, if helminths have been identified as a potential health hazard, the characterization aims to determine which species are endemic and to what extent.
Gather supporting information
STEP 2.4

## Slide 33
Bacteria
Enteric, transmitted by faecal-oral route.
Cause gastroenteritis, typhoid, E. coli diarrhoea
Cause severe health outcomes and long term effects
Excreta related pathogens
0.2 – 2 µm
hair
Visible
20 – 100 nm
Viruses
Can be excreted in very high numbers and are transported long distance in water.
Predominantly cause gastroenteritis, hepatitis A&E and viral meningitis.
3 – 20 µm
Protozoa
Enteric, cause gastroenteritis, Amoebic dysentery, giardiasis.
Production of cysts or oocysts enhance the survival in the environment.
1 – 300 µm
Helminths
Soil-based and water based-worms.
Ingestion of eggs or skin penetration.
Cause ascariasis, hookworms infections.
WHO Guidelines
Chapter 6
Pages 100-124

## Slide 34
Occurrence
Pathogens must be excreted into the environment in sufficient quantities by infected people
Excreta related pathogens
Environmental transmission of pathogens in faecal waste
Persistence
Pathogens must survive on surface, water, sewage and soil, and remain infectious
Vector or hosts
Presence and abundance of any required vectors or intermediary hosts
Infectivity
Specific strain and virulence
Individual’s susceptibility to infections
Immune status, nutritional status, age, pre-conditions
How do we detect pathogens in the environment?
WHO Guidelines
Chapter 6
Pages 114-119

## Slide 35
How do we detect pathogens in the environment? (Chapter 6.3.1 WHO Guidelines)
Excreta related pathogens
Environmental transmission of pathogens in faecal waste
Indicator of faecal contamination
In some circumstances, it might be important to identify the source and movement of an specific pathogen.
  bacteria
  viruses
  protozoa
E. coli as combined indicator
Also enterococci and bacteroides phage
Not perfect indicators!
But
Useful
Feasible
Economical
WHO Guidelines
Chapter 6
Pages 114-119

## Slide 36
Excreta related pathogens
Table 6.1
WHO Guidelines
Chapter 6
Pages 105-113

## Slide 37
Testing environmental samples for pathogens
Excreta related pathogens
Environmental transmission of pathogens in faecal waste
Sample collection and analysis of environmental samples for pathogens can be challenging and expensive.
In many cases, methods for analyzing human pathogens from environmental samples are not yet standardized.
Results could be different depending on the sample preparation and analysis.
obtain quantitative information on the concentration of pathogens in the sample.
You need:
Specialized team with equipment, experience and understanding of analytical methods.
Prepare a research plan, with specific objectives.
Goal:
evaluate the risk associated with contact or ingestion of the environmental sample.
evaluate the effectiveness of a treatment process.
Not always feasible. For SSP, E. coli indicator is sufficient.
or
WHO Guidelines
Chapter 6
Pages 114-119

## Slide 38
Helminths
Excreta related pathogens
Environmental transmission of pathogens in faecal waste
This is because:
Helminth infections are context specific.
Species and concentrations of Helminth eggs in waste influence the control measures.
Eggs infect snail that lives in standing waters.
Cercarie will swim and penetrate the skin of humans in the water.
It is important to understand which helminth are endemic in the locality of the SSP.
Examples of helminth infections
Transmitted by the faecal-oral route.
Contamination of produce grown with contaminated water and faecal sludge.
Eggs shed via faeces and the larvae penetrates the skin, usually at the feet.
Transmission route affects risk and required control measures
Schistosomiasis
Ascariasis
Hookworm infection

## Slide 39
Helminths: transmission of Schistosomiasis
Excreta related pathogens

## Slide 40
Helminths: transmission of Ascariasis
Excreta related pathogens

## Slide 41
Helminths: transmission of Hookworm infection
Excreta related pathogens

## Slide 42
Occurrence
Pathogens must be excreted into the environment in sufficient quantities by infected people
Excreta related pathogens
Environmental transmission of pathogens in fecal waste
Persistence
Pathogens must survive on surface, water, sewage and soil, and remain infectious
Vector or hosts
Presence and abundance of any required vectors or intermediary hosts
Infectivity
Specific strain and virulence
Individual’s susceptibility to infections
Immune status, nutritional status, age, pre-conditions
Why do we need to consider vectors in SSP?
WHO Guidelines
Chapter 6
Pages 114-119

## Slide 43
Excreta facilitated vector breading (Chapter 6.3.1 WHO Guidelines)
Excreta related pathogens
Environmental transmission of pathogens in faecal waste
Excreta, water and waste may serve as breeding sites.
Insects can act as vectors of disease by mechanically transporting pathogens in the environment.
Breed in excreta, such as pit latrines.
Carry human pathogens High microbial counts.
Enhance faecal-oral transmission, providing pathways from excreta to food or kitchen utensils.
Cockroaches:
Vector-habitat and mode of transmission must be considered in SSP
Flies:
Mosquitos
Carry a variety of enteric pathogens, including bacteria and protozoa.
Cause trachoma.
Improper drainage, stagnant water and ponds contribute to their breading.
Wide range of mosquito-borne diseases: dengue, malaria, West Nile virus, chikungunya, yellow fever…
WHO Guidelines
Chapter 6
Page 104

## Slide 44
Waste fractions from Step 2.2
Potential health hazards
Contextual and health data
Identify relevant health hazards
What information should we gather for our SSP?
Gather supporting information
STEP 2.4

## Slide 45
Information about disease conditions and pathogen concentrations:
Compiling biological hazard information
What should you collect?
Desktop literature
Public Health Authority
Consultation of personnel working in health facilities
From which sources?
Enteric (gastrointestinal) and urinary transmitted pathogens that exist in the community
Vector-borne diseases (e.g. mosquito borne malaria and dengue fever, rat borne)
Biological hazard information in relevant waste fractions (minimum: E. coli and helminth eggs)
Gather supporting information
STEP 2.4
SSP Manual
Guidance Note
2.5, Page 34

## Slide 46
Collect information on environmental parameters:
Compiling chemical and physical hazard information
What should you collect?
Environmental authorities
WWTP utilities monitoring results
Industrial entities or published references
Direct observation
From which sources?:
Chemical parameters and contaminants of solid and liquid waste streams of interest
Physical hazards that may be present in wastes or are of concern considering the working processes and practices
SSP Manual
Guidance Notes
2.6 and 2.7
Gather supporting information
STEP 2.4

## Slide 47
Collect information on the local climate and its variability:
Compiling key climate information
What should you collect?
Regional climate vulnerability assessment
Community knowledge
From which sources?
Records or history of extreme weather events
Future climate projections
Historical water quality data
Trends in water supply and land use
Assessment on climate hazards for water and other services
SSP Manual
Guidance Note
2.8
Gather supporting information
STEP 2.4

## Slide 48
Depends on:
What is really needed? Range of relevant information needed.
What is available? Data availability (e.g. secondary data) and quality.
What resources are available? Resource considerations (financial, human, time).
Range and quality of data
Official health reports, statistics
Literature and research articles
Direct observation
Participatory data collections
Data that should be sufficient:
Environmental sampling
Epidemiological studies
Environmental assessments
Nice to have:
Gather supporting information
STEP 2.4

## Slide 49
To ensure that the system description is complete and accurate.
Previous steps probably largely a desk exercise.
There is a need to check through field investigations to ensure that the information is complete and accurate.
Tools: sanitary surveillance, transect walks, focus group tools etc.
Validate claimed treatment efficiency by references, testing programmers etc.
Map, system description and waste fraction characterization need to be updated after validation.
Confirm the system description
STEP 2.5

## Slide 50
Step 2.4. Gather supporting information
Step 2.5: Confirm the system description

## Slide 51
Applying Steps 2.4 to 2.5 to your SSP
Using participant’s worksheets for Module 2, within your groups:
GROUP WORK
Write down any information that will affect SSP development and implementation the system.

## Slide 52
MODULE 2:
DESCRIBE THE SANITATION SYSTEM