## Slide 1
SSP Manual
Pages
81 to 89
MODULE 5:
MONITOR CONTROL MEASURES AND VERIFY PERFORMANCE

## Slide 2
Why monitor and verify?
Sanitation systems are dynamic – things change in the short or long term.
Any system can under-perform – leading to unacceptable public health risks and loss of confidence in the service or products.
Need to provide assurance that the entire system is operating as intended.
MODULE 5:
MONITOR CONTROL MEASURES AND VERIFY PERFORMANCE

## Slide 3
Module 5 answers the question:
“Is the system operating as planned?”
MODULE 5:
MONITOR CONTROL MEASURES AND VERIFY PERFORMANCE

## Slide 4
5.1 Define and implement operational monitoring.
5.2 Verify system performance.
5.3 Audit the system.
• An operational monitoring plan.
• A verification monitoring plan.
MONITOR CONTROL MEASURES AND VERIFY PERFORMANCE

## Slide 5
Hazard, hazardous event, effect, risk, ...!?
MODULE 5:
MONITOR CONTROL MEASURES AND VERIFY PERFORMANCE
Operational Monitoring
How effective are the control measures?
Verification Monitoring
Does the system meet the intended performance outcomes?
Hazardous event
Hazard(s)
Health effects
Risk
Likelihood
Severity
Control
measures

## Slide 6
To give simple and rapid feedback on system performance, so that corrections can be made quickly, if required.
SSP Manual
Page
83
Operational Monitoring
Frequent.
Many monitoring points throughout the system.
Simple observations and tests.
Used to manage risks before they occur.
Implemented by service provides
Routine monitoring to inform management decisions.

## Slide 7
Operational monitoring collects and uses
Simple observations and measurements
Sampling and testing

## Slide 8
Possible monitoring parameters for each sanitation step:
Toilet
State of cover slab.
Visible/reported overflows.
Availability, accessibility and privacy of toilet facilities.
Cleanliness.
Containment-storage/treatment
Inspection of dwellings and buildings
Routinely, in periodic/ special surveys or in the national census
Inspection of dwellings and buildings
Routinely, in periodic/ special surveys or in the national census
WHO Guidelines
Section 4.6.2
Page 70
SSP Manual
Guidance note
5.1, Page 83

## Slide 9
Short-standardized observation checklists that can be adapted and used by stakeholders to assess risk factors at or near sanitation facilities.
WHO Sanitary Inspection Forms

## Slide 10
Use of PPE by sanitation workers
Use of the pre-defined roads
Cleanliness of sewers
Transport and conveyance
Treatment
Data collected from customers, formal and informal operators and, where relevant, licensing authorities or regulatory bodies.
Flow rate
Retention times
Composting temperatures
Data collected from operators and verified by occasional sampling and independent laboratory analysis.
Possible monitoring parameters for each sanitation step:
WHO Guidelines
Section 4.6.2
Page 70
SSP Manual
Guidance note
5.1, Page 83

## Slide 11
End use/ disposal
Correct application / irrigation process.
Duration of withholding periods.
Inspection of nearby farms
Routinely, in periodic surveys
Possible monitoring parameters for each sanitation step:
SSP Manual
Guidance note
5.3, Page 86

## Slide 12
May not be practical to monitor all control measures.
Decide which control measures need to have operational monitoring (prioritize based on risk assessment).
Critical limits help decide acceptability:
usually numerical limits based on a parameter measurement.
qualitative limits may be appropriate (e.g. “all odours to be acceptable” or “flies not a nuisance”).
TIPS
Keep in mind…

## Slide 13
Suggested recording format
SSP Manual
Tool 5.2
Page 84

## Slide 15
To periodically verify whether the system meets the intended performance outcomes.
Verification
Periodic.
Few points, but focused on the system-end points (quality of the effluents).
More complicated tests (e.g. E.coli, Helminth eggs).
Used to prove the system works.
Might be undertaken by the operator or surveillance agencies.
It checks the effectiveness of the implemented control measures.
SSP Manual
Page 86

## Slide 16
Microbial testing of crops, fish products, and waters at exposure points and system boundaries, e.g. E.coli and Helminth eggs.
Examples of typical verification data
Toilet
Use of toilet facilities (decrease of open defecation)
Containment-storage/treatment
Conveyance
Treatment
End use/ disposal
Amount of faecal sludge transported to the faecal treatment system.
Pathogen concentration in groundwater
Microbial testing of effluents, e.g. E.coli and Helminth eggs.
SSP Manual
Guidance note
5.2, Page 86

## Slide 17
To provide additional independent evidence of the system performance and quality of the SSP.
Might not be feasible in the initial stages of SSP implementation.
Check the quality and effectiveness of the SSP implementation.
Ensure that the SSP contribute to health outcomes.
Can be done by internal, regulatory or independent auditors.
Demonstrate that the sanitation safety plan has been properly designed, is being implemented correctly and is effective.
Audit the system
STEP 5.3
Audits:
SSP Manual
Page 88

## Slide 20
GROUP WORK
Applying Module 5 to your SSP
Use table group worksheet Module 5 for instructions.
Within your groups:
For the 3 selected control measures, prepare the operational monitoring plan.
For the 3 selected control measure, prepare the verification plan.

## Slide 21
MODULE 5:
MONITOR CONTROL MEASURES AND VERIFY PERFORMANCE